## Slide 1: Flood resilience in the water sensitive city
Richard Ashley , Chris Zevenbergen, Berry Gersonius
Assela Pathirana, Mohan Radhakrishnan, Jeroen Rijke
Amar Nanda, William Veerbeek
Flood resilience group, IHE, Delft
CRC for Water Sensitive Cities
An overview of four years of development of the processes to embed flexibility, adaptability and hence resilience into the Water Sensitive City via Water Sensitive Urban Design (WSUD)

## Slide 2
The work presented has been developed in the Flood resilience Group at IHE, Netherlands
And as part of the Co-operative research Centre for Water Sensitive Cities in Melbourne, Australia

## Slide 3: Lots of ideas and methodologies
In UK - Lessons and guidance from a number of ongoing projects:
UK: CIRIA urban drainage
  http://www.susdrain.org/
Australia/Netherlands: CRC for Water Sensitive Cities
  https://watersensitivecities.org.au/

## Slide 4
What we used to do

## Slide 5
Inherently imperfect:
Highly dynamic environment
Large uncertainty in (flood risk) estimation
Investments upfront, benefits remote (and uncertain)
Change will happen in the lifetime of the artefact
How can we design now when we don’t know what will happen?
Need to avoid lock-in and lock-out
Cities most vulnerable places!

## Slide 6: 4 principles
Manage water to deal with both water scarcity and water excess
Manage and utilise the water cycle as locally as possible
Deal with water appropriately and synergistically within urban environments
Integrate water management effectively into the wider (urban) systems, services and utilities

## Slide 7
RAINFALL - RUNOFF
Ocean processes water levels, tides and waves
Rivers, streams, lakes etc.
Water levels and flows
Groundwater
Water levels
Natural waters
Urban areas
Pluvial flooding
Groundwater flooding
Fluvial flooding
Coastal flooding
Water supply, place making, aesthetic and urban design opportunities
All forms of water provide opportunities

## Slide 8: There are many frameworks
Each purporting to provide aspects of adaptation/resilience etc.
Europe has been more focused on flooding than Australia (heat and drought)
But, Australia has a long history of developing ideas on water sensitivity and practice

## Slide 9: The CRC for water sensitive cities programme
$Aus 120bn + programme over 9 years
Now in tranche 2 project programme
Tranche 1 (2012-2017):
  How do our culture, institutions, and human systems affect the adoption of new ideas and innovation?
  How will changes in our natural environment impact on and affect how we plan and build our cities?
  What technologies and information are needed to support delivery of water sensitive cities?
  What are the range and appropriate mix of interventions to translate research and knowledge into practice?
Tony Wong

## Slide 10
A vision for a Water Sensitive City
LIVEABLE
RESILIENT
SUSTAINABLE
PRODUCTIVE
As described in the vision for the CRCWSC, a water sensitive city can also be described as one that is resilient, liveable, productive, and sustainable.

## Slide 11
“Mitigate flood risk and damage; and create public spaces that collect, clean, and recycle water.”

## Slide 12: Tranche 1
Programme components
  A: Society
  B: Water Sensitive Urbanism
  C: Future technologies
  D: Adoption pathways
IHE: Social-Technical Flood Resilience in Water Sensitive Cities – Adaptation across spatial & temporal scales (Project B4.2)

## Slide 13: Social-Technical Flood Resilience in Water Sensitive Cities – Adaptation across spatial & temporal scales (Project B4.2) - objectives
Formulate guidance as to how to utilise the developing knowledge from Dutch (and other EU) flood risk management practices (e.g. Multi-Level Safety) within an Australian context.
Review and propose how best the (three) domains of Flood Risk Management defined in by TU Copenhagen can be included in the Adaptation Tipping Point (ATP) method.
Define how Australian cities can couple adaptation for flood risk with ‘normal’ (re)development and infrastructure projects to become normal practice.

## Slide 14: Further B4.2 objectives
Devise an integrated approach so that the (3) domains of Flood Risk Management can be best brought together and served by mainstreaming the opportunities derived from the application of the Adaptation Mainstreaming Opportunities (AMO) method.
Further develop the existing Real-In-Options (RIO) accounting tools already being applied to adapt Flood Risk Management systems to climate change.
Investigate how the approaches above inform regulation into the future and acceptability, expectations and changes to quality of life in urban areas and how socio-economic processes may best be influenced.
Incorporate the above into the risk model (developed by TU Copenhagen) and demonstrate/apply the above for cases.

## Slide 15
Adaptive
Planning
4
3
2
1
Adaptive Planning to cope with future uncertainties
Robustness
Flexibility
Notes: With the development of the call war, were the role of scenario based planning based on limited information really got going. The Rand corporation, which initially started as a R&D facility for the US military has a pivotal role in this. These days, we such frameworks for more peaceful purposes where adaptive planning is especially used as an policy framework to cope with future uncertainties. Although many different methods have been developed within the adaptive planning context, many have two ingredients in common: Robustness and flexibility. Robustness as approach to ensure risk distribution and flexibility to cope with future changes for which currently information is lacking. If you allow me, I take the opportunity to mention to big buzzword here: resiliency. Adaptive planning approach aiming to increase the resiliency of a system, area…and in our case: the city. Which brings me back to Rotterdam. Now what is special about Rotterdam, is that they’re actually managed to make the theory operational. They use it in their climate adaptation planning but more importantly: it shows in the projects they’ve put on the ground in the past decade.

## Slide 16: Developing Robustness: 4 Domain approach
Increase in impact / consequence
Extreme event
Exceedance event
design event
Everyday event
Emergency response & spatial
2
3
4
1
Rainfall or other event
Design for exceedance
- WSUD
Conventional responses & WSUD
WSUD
Increase in event magnitude
Design approach
The missing domain
- Water on the surface
WSUD: Integrating Water and Urban Design to deliver added value to the city
Notes: Now if we are engineers, we typically focus on design events. They define the standards on which we base our proposals;
If we are architects, we typically focus on everyday events; on how to maximize usability and all the socio-cultural values we incorporate in our design;
Yet rarely, we think of how are proposals function beyond the requirements, or even during extreme events.
Now one of the things Rotterdam does very well, is to develop options that cover more of these domains. Furthermore, they always seek multiple benefits; ways to provide additional value for the city and its inhabitants

## Slide 17
Several reports
Journal papers
2 PhD theses
https://watersensitivecities.org.au.

## Slide 18
ABC news, 10/7/2017
Adaptive ecosystem management: why, when & how to cope with climate change?
PhD : Amar Nanda
Notes: when do we act?

## Slide 19: Multi-layered safety
Protection (layer 1): taking measures to reduce the likelihood of floods;
Prevention (layer 2): using spatial planning and adaptation of buildings to reduce damages;
Preparedness (layer 3): improving organizational preparation;
Emergency relief (layer 3): providing emergency relief;
Recovery and lessons learned (layer 3).
Salinas Rodriguez, C., Ashley, R., Gersonius, B., Rijke, J., Pathirana, A., Zevenbergen, C. (2014) Incorporation and application of resilience in the context of water sensitive urban design: Linking European and Australian perspectives. WIREs Water. Volume 1, Issue 2. March/April Pages 173–186

## Slide 20: How does the MLS apply to drought planning?
Cases examined for Melbourne, Sydney and Adelaide
Rijke, J., Smith, J.V., Gersonius, B., Herk, S.v., Pathirana, A., Ashley, R., Wong, T., Zevenbergen, C. (2014). Operationalising resilience to drought: multi-layered safety for flooding applied to droughts. Journal of Hydrology, 519, 2652-2659 doi: http://dx.doi.org/10.1016/j.jhydrol.2014.09.031

## Slide 21: Maximising value from water beyond flood and drought resilience
Clear that liveability can be enhanced
New tools to account for this emerging
Gersonius B., Rijke J., Ashley R M., Bloemen P., Kelder E., Zevenbergen C. (2016). Adaptive delta management for flood risk and resilience in Dordrecht, the Netherlands. Natural Hazards, 2: 201-216.

## Slide 22: Mainstreaming (piggy backing)
Integrating flood risk and water management into urban design
- Mainstreaming (connecting) with urban (re)development

## Slide 23: Brought together in the 4RAP model

## Slide 24: Type of measure linked to area characteristics

## Slide 25: The revised 3DAs – the 4DA approach

## Slide 26
2
1
WATER SQUARE BENTHEMPLEIN
Design Events: Developing Multiple benefits
Disconnects stormwater from adjacent roofs (day-to-day);
Creates a peak storage (design events);
Design in collaboration with students, i.e. end-users (multiple benefits);
Design: De Urbanisten, Rotterdam
Peak storage

## Slide 27
Design Events: Developing Multiple Benefits
2
1
3
Design: De Urbanisten, Rotterdam

## Slide 28
Community garden
Design Events: Developing Multiple Benefits
2
1
3
WATER SQUARE BELLAMYPLEIN
Design: Gemeente Rotterdam
Creates a peak storage (design events; exceedance events);
Multi-purpose neighbourhood square (multiple benefits);
Notes: 15 times a year, max. 15 cm water; 6 times a year >15 cm, 1x time year max. 0.5m water.

## Slide 29
Urban playfield
2
1
3
Design Events: Developing Multiple Benefits
WATER SQUARE FREDERIKSPLEIN
Design: Gemeente Rotterdam
Creates a peak storage (design events; exceedance events);
Playfield (multiple benefits);

## Slide 30
Developing an integrated design across scales
Design: De Urbanisten, Rotterdam
2
1
3
Diversification of stormwater management system;
Integrating management of day-to-day, design and exceedance events;
Maximizing benefits from blue-green infrastructure;
Seeking true design integration instead of ad-hoc measures
WATER SENSITIVE ZOMERHOF KWARTIER

## Slide 31
ROOFPARK VIERHAVENSTRAAT
Ensuring Standards & Developing Multiple Benefits for Day-to-Day use
2
1
Design: Buro Sant & Co, The Hague
Part of primary flood defence system (1:10,000 standard)
Integration of flood defence, park and retail area;

## Slide 32
Connects 2 formerly separated neighbourhoods;
Creates a unique neighbourhood park;
Adopted by local community (maintenance), safety;
Cost reduction through integration;
Design Events: Developing Multiple Benefits
2
1
Design: Buro Sant & Co, The Hague

## Slide 33
2
1
Design: Buro Sant & Co, The Hague
Ensuring Standards & Developing Multiple Benefits for Day-to-Day use
Notes: What is essential is that this area transformed from a derelict railway area and a river dike into a highly used neighborhood park and shopping area. So from a area that separates into an area that connects.

## Slide 34
Exceedance events: Ensuring easy recovery
3
Design: Gemeente Rotterdam
URBAN FLOODPLAIN WESTERSINGEL

## Slide 35
3
2
1
Design for Exceedance & Multiple Benefits for Day-to-Day use
PEAK STORAGE KLEINPOLDERPLEIN
Design: Gemeente Rotterdam
Creates a peak storage (design events; exceedance events);
Park function (multiple benefits);

## Slide 36
Water storage / sports
Water storage / parking garage
Water storage / housing
Water storage / attractive public area
Mainstreaming water into urban development
Notes: So far the theory…but how about the practice?
In order to be prepared for a changing future we do have to take measures now.
As it is difficult to create more new water bodies within the city boundaries we have to find smart combinations with other urban functions.
Like the combinations of this water storage lake and houses, or, more close into the city centre this water storage reservoir beneath the driveway of a parking garage.
Another nice example is the so called BLUE connection in the southern part of Rotterdam:
This partial new waterway will have three functions:
Water storage and Supply of clear and high quality water towards the highly dense urban area of Rotterdam;
Recreative waterway for small vessels and canoeing; and
Ecological connection in the Rotterdam region
this connection will also increase the value of the real estate and the surrounding areas
This approach requires an early intervention of planning processes. Spatial planning processes in part of the world are generally very slow, so we have to claim the essential space in an early stage. This asks for long term perspectives as we created in the Waterplan 2 Rotterdam.

## Slide 37
2400 m3 water storage
in shells on the roof of parking garage
Central train station
Ensuring Standards: Mainstreaming water into urban development
1
Design: Maarten Struijs/Gemeente Rotterdam
Notes: In all these projects, water has been the primary driver. But sometimes, it’s the other way around.

## Slide 38: Recovery phase: Impoldering
Self-reliant Island of Dordrecht

## Slide 39
The Merwedestraat-Oranjelaan connects the city center and the unembanked ‘Stadswerven’ area with the N3.
When elevated at certain places, it could potentially function as a life-line for the unembanked ‘Stadswerven’ area.
Large maintenance works are planned for 2015-2016.
Looking at mainstreaming - maintenance of access road

## Slide 40
After assessing the feasibility of mainstreaming in 3 projects, it appears unlikely under the current conditions that the scope of any of the projects will be widened to include flood risk management
However, the dialogues about this have been beneficial in other ways:
  Alignment of current projects
  Need for critical reflection on how existing planning provisions (MIRT study) can better enable mainstreaming
  Increased awareness about flood risk management objectives amongst project managers
Conclusions from trying to mainstream in Dordrecht

## Slide 41: Dordrecht – the combined domains approach (Domain 1 not shown) compared with the traditional

## Slide 42
Points at which the magnitude of change is such that the strategy can no longer meet its objective
Adaptation tipping points

## Slide 43: Adaptation (deficits/gaps)
https://www.youtube.com/watch?v=ieiFJAlGtCs&t=14s
https://assela.pathirana.net/index.php?title=Urban_adaptation_in_rapidly_growing_cities_need_a_paradigm_shift

## Slide 44: Adaptive policy pathway

## Slide 45: A standard procedure for incorporating flood resilience into a water sensitive city

## Slide 46: Detailed guidance
When, where and how to adapt
  A simple guide to adapting
Mainstreaming opportunities and framework
Building in flexibility
Tools: tipping points; adaptation pathways; real (in) options analysis
Gersonius B., Ashley R., Jeuken A., Pathinara A., Zevenbergen C. (2015). Accounting for uncertainty and flexibility in flood risk management: comparing Real-In-Options optimisation and Adaptation Tipping Points. J. Flood Risk Management (8) 135-144. DOI: 10.1111/jfr3.12083

## Slide 47: Flexibility In Adaptation Planning: When, Where And How To Include Flexibility For Increasing Urban Flood Resilience PhD: Mohanasundar Radhakrishnan

## Slide 48: Case studies in Can Tho and Melbourne

## Slide 49
Source: Gemeente Rotterdam
Sea level rise
years from now
Effectiveness of measures
Develop adaptation pathways based on combinations of measures
Developing Adaptation Pathways
Notes: Lock-ins, no-regrets, low regrets, etc..

## Slide 50
Evaluate pathways map
targets begin to be missed after four years
there are four options
A and D should be able to achieve the targets for the next 100 years
There are several scenarios for climate change
If Action B is chosen, a tipping point is reached within about five more years; a shift to one of the other three actions (A, C, or D) will then be needed to achieve the targets
https://publicwiki.deltares.nl/display/AP/Pathways+Generator

## Slide 51: Learning from the financial markets
Real Options:
  (i) possessing options - i.e., creating a chance now that is laid out into the future to work with uncertainty;
  (ii) exercising the option, i.e., converting the option into an opportunity at the time of convenience.
i.e. such options enable the creation of value from uncertainty

## Slide 52: Sequential approaches
An adaptation pathways approach builds flexibility by sequencing the implementation of adaptation measures, so that the risk management system can adapt to changing conditions.
A real options approach values the sequenced adaptation measures in financial terms and helps in determining the sequence of adaptation measures that has the best value for money based on the probability of scenarios.

## Slide 53: What else is needed?
Local contexts
Knowing where the flexibility is best embedded
Interactions between systems

## Slide 54
Blue-green infrastructure:
increasingly serving as multi-functional flood exceedance pathways designed to cope when the formal drainage systems are overloaded

## Slide 55
Radhakrishnan, M., Pathirana, A., Ashley, R. and Zevenbergen, C. (2017). Structuring Climate Adaptation through Multiple Perspectives: Framework and Case Study on Flood Risk Management. Water, 9 (2), 129. doi: 10.3390/w9020129.
Responding to flood risks in Elster Creek catchment, Melbourne
A singular perspective example
Twitter: @UnescoIHE

## Slide 56: Elster Creek, Melbourne
Melbourne suburb
Elwood (Sea side of Elster creek)
  City of Port Phillip
  Area: 2.6 km 2
  Originally a swamp, drained by Elster creek drain
  Population: 14,638 (2011 Census)
  No. of dwellings: 8332
  Terrain: Relatively flat
Experiences Pluvial, riverine and flash floods

## Slide 57
Future flooding by 2100
The flood damages are especially sensitive and have a wide uncertainty for rainfall and sea level rise effects on Elster creek
http://www.3aw.com.au/news/heavy-rain-causing-havoc-on-victorian-roads-20161229-gtjg24.html

## Slide 58: Flooding in Elwood – 30 Dec 2016
http://www.theage.com.au/victoria/elwood-residents-mop-up-after-flash-floods-but-fear-flooding-will-continue-20161230-gtjqjq.html
http://www.3aw.com.au/news/heavy-rain-causing-havoc-on-victorian-roads-20161229-gtjg24.html

## Slide 59: Flexible adaptation planning (process)
Adaptation pathways:
  High level route map of measures
  Pathways based on tipping points
Real in options
  focusses on providing value for the flexibility inherent in having the future options such as dikes
The value is in making the adaptation flexible in terms of implementing the measure (when) and determining the value of flexibility based on the timing (how much).
But, where best to incorporate or embed flexibility?

## Slide 60: Borrowing from the car industry - Flexible platform design process – to ensure agility
The identification of components as a candidate for flexibility is based on the magnitude of change that the components propagate throughout the system when they are changed
Flexible platform design process in the automobile manufacturing sector
( Adapted from Eckert et al. 2004) )
Notes: According to Eckert et al. (2004) the components that are capable of propagating greater change are to be assessed carefully before being selected as candidates for embedding flexibility. For example, in the design of an automobile chassis, one of the parameters that determines its dimensions - the length and breadth - is the size of the engine. The size of the engine in turn depends on the number of cylinders. While designing the chassis, the width is kept constant for all the variants to limit change propagation. This is because change in width has a direct bearing on the stability of the vehicle. The change propagation of chassis width is generally much higher compared with that of the chassis length. Hence the length of the chassis is a flexible design parameter that can be changed using differently sized physical components. Enabling flexibility in such design parameters requires initial investment in design, tooling and assembly equipment and is similar to using real in options (RIO) in chassis design (Suh et al. 2007).

## Slide 61
Flexible adaptation planning process for Water Sensitive city (WSCapp )
Notes: Flexible adaptation planning process for Water Sensitive city (WSCapp ). The white arrows enclosed in black lines represent the sequence of steps in the WSCapp (clockwise). The chequered arrow from step 8 to step 1 represents the feedback to the vision cycle when a change in vision or objective happens over the time. The thin broken arrow from step 8 to step 5 represents the iteration with in the WSCapp, in case the final portfolio of measures obtained after the first run are not satisfactory. You have nicely set out the case that visions change over time – but the figure does not show a feedback to the vision circle. I am also unsure what the arrow in the middle means?

## Slide 62: Range of possibilities

## Slide 63: Relative uncertainty
Decide which measures can be robust and which can be flexible
  Road elevation to prevent coastal flooding?
  Rainwater harvesting
  Flood proofing of households
  Flood detention in parks
  Retrofitting of drainage systems

## Slide 64: Interactions and Inter-relationships
Identification of components based on inter-relationships
Possible categorisation of flexible measures
Flexible Resilience and sustainability components (e.g. rainwater harvesting)

## Slide 65
Develop pathways map (RCP 2.6 scenario)

## Slide 66
Develop pathways map (RCP 8.5 scenario)
This switch occurs sooner
And does not work for as long

## Slide 67: Costs and benefits
Adaptation Measures | Tipping Point (Year) |  |  |  | Present value of total cost of flood damages and implementation cost of adaptation measures (in Million AUD) |  |  |  | Expected Value across scenarios (in Million AUD) | Range of Benefit – Cost Ratio
 | RCP 2.6 | RCP 4.5 | RCP 6.0 | RCP 8.5 | RCP 2.6 | RCP 4.5 | RCP 6.0 | RCP 8.5 |  | 
No measure | 2015 | 2015 | 2015 | 2015 | 584 | 635 | 667 | 762 | 662 | -
A | 2033 | 2020 | 2019 | 2017 | 1,270 | 1,304 | 1,321 | 1,410 | 1,326 | 0.3 to 0.16
B | 2015 | 2015 | 2015 | 2015 | 338 | 370 | 391 | 463 | 391 | Circa 1.0
C | 2015 | 2015 | 2015 | 2015 | 451 | 471 | 486 | 516 | 481 | 1.71 to 1.35
A & C | 2090 | 2090 | 2090 | 2086 | 1243 | 1282 | 1290 | 1318 | 1,283 | 0.3 to 0.2
C & A | 2090 | 2090 | 2090 | 2086 | 1,365 | 1,460 | 1,482 | 1,560 | 1,467 | 0.3 to 0.2
C & B | 2090 | 2090 | 2090 | 2073 | 334 | 348 | 357 | 382 | 355 | 2.4 to 2.1
B & C | 2090 | 2090 | 2090 | 2073 | 334 | 348 | 357 | 382 | 355 | 2.4 to 2.1
Adaptation Measures: A – Drainage retrofitting; B – Rainwater harvesting; C– Flood proofing households |  |  |  |  |  |  |  |  |  | 

## Slide 68: Choice
Final decision can be based on expected value, benefits, costs or any other stakeholder defined criteria
From PV of costs the recommended adaptation measures are both at household scale:
  Rainwater harvesting
  Flood proofing of households
Although the most effective pathway begins with the new foreshore Mangrove forest

## Slide 69
Radhakrishnan (2017)
Managing changing flood risk in Can Tho, Vietnam
A multiple perspective case:
A combination of criteria - minimal construction cost, avoided flood damages and eco-system benefits converts the climate adaptation ‘problem’ into a multiple objective problem/opportunity and help in choosing pathways that satisfy all of the objectives.
Twitter: @UnescoIHE

## Slide 70: Multiple interacting perspectives/objectives
Adaptation planning
Context specific adaptation - Relationship between drivers and adaptation measures
Structuring adaptation responses
Application of context specific precedence grammar logic (Islam T., 2016)

## Slide 71: Whose adaptation?
roads
hospitals
water
heat
commerce

## Slide 72: Detailing the multiple perspectives
Detailed analysis of putting together multiple perspectives is complex
How can we overcome the challenge of modelling and evaluating a complex adaptation problem that has been structured using a multiple perspective adaptation framework?
How can we model the path dependencies in a multiple driver context?
Decision making based on temporal and operational interdependence
Risk based framework based on “Risk of Failure” triggers
Context specific adaptation pathway generation and evaluation

## Slide 73: Adapting to flooding in Can Tho, Vietnam

## Slide 74: Context specific grammar in Can Tho 2. Adaptation modules
Notes: By using the determinants for adaptation measures (Table ) an adaptation pathway set ‘W’ comprising pathways have been generated using the rule set ‘R’ complying with the context specific adaptation grammar (algorithm). Although there are only six adaptation modules, excluding the base case where there is no adaptation measures, it is possible to generate multiple combinations that satisfy the rules in rule set ‘R’. For example, to implement a 70 cm dike module ‘6.0’, the pre-requisite is the foundation module ‘5.0’. When a ‘5.0’ is in place, it is possible to implement a 20 cm dike ‘2.0’ or a 50 cm dike ‘4.0’ or a 70 cm dike ‘6.0’. Hence the pathway to ‘6.0’ could comprise there being no smaller dikes, one smaller dike or both of the smaller dikes. Thus the adaptation pathway set ‘W’ comprising 78 possible pathways has been generated. A number of the adaptation pathways generated are shown in Figure as examples. The next step after generating the pathways set ‘W’ comprising all the pathways is to determine the timing of the switch from a lower dike to a higher dike for all possible scenario combinations ‘Strig’.

## Slide 75: Context specific grammar in Can Tho 4. Evaluation of adaptation pathways
Least preferred pathways
Preferred pathways
Colours represent different pathway combinations
The largest circles are those with the greater probability of occurrence
Pathways 0, 1 and 4 have the highest ranking for the most probable scenarios
Notes: The pathways are ranked into an ascending order. The pathway that has a low total cost across the majority of the scenarios is the preferred path, whereas the pathways with highest total costs are the least preferred path (Figure). The pathways 0-9 are depicted along the x-axis from left to right, whereas the relative ranking of the pathways are presented on the y-axis. The least preferred pathway with lower rank –denoted by a bigger number - is at the bottom, whereas the most preferred pathway with the highest relative rank is at the top of the y-axis. The coloured circles represent the evaluation scenario combination ‘Seval’ and the probability of occurrence of the scenario combination. The colour of the circle represents a particular scenario combination ‘si’, whereas the size of the circle represents the probability of occurrence of a particular scenario. The bigger the circle, the more likely the scenario is to occur. From Figure it can be seen that the pathways 0-5 have higher ranking across most of the scenarios, whereas pathways 6-9 have lower ranking across most of the scenarios. Hence the decision makers in Can Tho can focus on pathways 0-5 to select the desired pathway. The other decision criteria could be the performance based on the likelihood of scenarios. Among pathways 0-5, the pathways 0, 1 and 4 have higher ranking for scenarios that are more likely to occur. Pathways 5-9 also rank low in the scenario that is most likely to occur; as the size of the dark green circles in the pathways are bigger and also ranks lower. Hence the focus can be narrowed down to the pathways 0, 1 and 4. Pathway 1 has the highest relative rank ‘1’ in a scenario that is most likely to occur.

## Slide 76: Pathway 1
At sequential trigger points:
70cm dike foundation
20cm dike
50cm dike
70cm dike

## Slide 77
Identify and evaluate actions
How to ‘sell’ all this to decision makers?
  They only want robustness
Look out for lock-ins and lock-outs
Identify the bounce forwards opportunities
Mainstream and leverage
Challenge ‘we have always done it that way’
Speak truth to power……

## Slide 78: Summary
There is a wealth of information available on the CRC Water Sensitive Cities home page
  https://watersensitivecities.org.au/
There are also many journal and conference papers
Probably the most significant aspect of the IHE contribution has been to set out the options and opportunities in clear and straightforward reports for practitioners